## Slide 1: lightweight PUB/SUB for WEB APPS using MQTT
Jason Follas Sr. Software Engineer Quicken Loans

## Slide 2: Abstract
MQTT is an extremely lightweight publish/subscribe messaging transport. It is commonly used as a machine-to-machine connectivity protocol for IoT devices, and usually runs over TCP/IP using sockets. But, recent efforts have implemented the protocol in JavaScript using web sockets, making it possible to use MQTT from within a web browser. This session will introduce the MQTT protocol, discuss various brokers, talk about messaging and Quality of Service, and provide examples of how to use Pub/Sub to enhance your web application and interact with IoT devices.
Notes: MQTT
Problem definition (IoT, wearable, etc)
- Distributed network of devices communicating
- Battery or limited power
- Unreliable networks (cellular, satellite, wireless in general)
Agenda
- Introducing MQTT
- What is Publish / Subscribe
- Client, Broker, connection
- MQTT Publish, Subscribe, Unsubscribe
- MQTT Topics
- MQTT Quality of Service
- Persistent Sessions and Queueing Messages
- Retained Messages
- Last Will and Testament
- Keep Alive and Client Take-Over
- Demo
Lightweight pub/sub protocol with reliable bi-directional message delivery
Key aspects
- High volume of data in low bandwidth networks
- Small code footprint
- Runs on top of TCP/IP
- Avoids polling
- Event oriented
- Recovery, store and forward, and pub/sub are part of the implementation
Topic: ASCII string
Connection is initiated by client - helpful for NAT
CONNECT ->
<- CONNACK
Client ID: Unique ID (per broker)
Clean Session (false: QoS 1 and 2 messages will be stored if client goes offline and delivered on next connection)
Username/Password
Will: If unexpected disconnect, broker sends Will message to the Will topic on the client's behalf
Keepalive
Publish
Topic name
QoS
Retain-flag: Broker can save one message per topic to automatically provide to new subscriptions (vehicle odometer problem if car is offline)
Payload: Binary
Packet Identifier
DUP flag
Subscribe
Packet Identifier
List of subscriptions
Persistent Session:
- All subscriptions maintained while offline
- All QoS 1/2 messages not confirmed by client
- All new QoS 1/2 sent while offline
Retained messages:
- "last good message" for the topic
- To delete, send a zero byte payload as retained
Keep Alive and Client Take-Over
- TCP/IP does not always notify when a socket breaks. Broker could think connection is alive but really is dead.
- Client must send a command or keepalive message periodically (defined by client at connection)
- Max keepalive is 18h 12m 15s (65535 seconds)
- Takeover is when a client connects using the same client id of a session that the broker thinks is still connected. Prev is closed, and new connection takes over prev
MQTT vs HTTP
MQTT overhead is about 20% of HTTP
Where used:
- POS
- Slot machines
- Automotive/Telematics
- Medical
- Home Automation
- Railway
- Asset Tracking/Management
- Space probe communication (?)
- Oil, Gas, Solar
Facebook Messenger:
- First pass had issues with long latency. Was reliable but slow.
- With only weeks before launch, refactored to use MQTT
- Designed to use bandwidth and battery sparingly (important for mobile apps)
- "By maintaining a MQTT connection and routing messages through our chat pipeline, we were able to often achieve phone-to-phone delivery in the hundreds of milliseconds rather than multiple seconds"
Amazon AWT IoT
Microsoft Azure IoT Hub

## Slide 3: The Petroleum Pipeline Problem

## Slide 4
Shutterstock

## Slide 7: Oil Pipeline
Equipment and Sensors (data origination):
  Equipment status
  Pump status
  Pump Bearing temperature
  Product temperature
  Flow rates
  Valve status
  Valve control
  Tank levels
  Etc.
One very important data consumer: SCADA host system
  (Supervisory Control and Data Acquisition)
Need to deliver real-time data to SCADA

## Slide 8: 1998
Pentium II 300MHz
128MB RAM
9GB Hard Drive

## Slide 10: Goals
Energy-friendly and low-bandwidth protocol for connecting oil pipelines using satellite connections
  Simple to Implement
  Quality of Service for Data Delivery
  Low processor/memory requirements
  Bandwidth efficiency (wireless communication costs were significant in 1999)
  Data Agnostic
  Continuous Session Awareness
  Multiple simultaneous data consumers

## Slide 11: Their Solution

## Slide 12: Solution: MQTT
MQ Telemetry Transport
Invented 1999 by Andy Stanford-Clark (IBM) and Arlen Nipper (Arcom/Cirrus Link/Eurotech)
Used internally by IBM, v3.1 released royalty free in 2010.
MQTT is no longer an acronym

## Slide 14: What is MQTT?
A binary-based protocol
built on top of TCP/IP that
enables publish/subscribe
for machine-to-machine communication

## Slide 15: Not a Message Queue
Was a transport protocol for IBM MQ Series, but has no traditional queues itself

## Slide 16: Standards
OASIS standard (MQTT 3.1.1) as of 2014
IANA TCP ports 1883/8883

## Slide 17: Publish/Subscribe

## Slide 18
IoT Device
Application
Mobile Device
Web App
Broker
Publish
Publish
Publish
Publish
Subscribers
Publisher
Sensors

## Slide 19: Some Brokers
Mosca (node.js)
Mosquitto (Python)
Emitter (.NET)
emqttd (Erlang/OTP)
VerneMQ (Erlang/OTP)
RabbitMQ (via plugin)
HiveMQ (“Enterprise” Broker)
Azure IoT Hub
AWS (Amazon) IoT Message Broker

## Slide 20: MQTT VERBS
Connect
Disconnect
Subscribe
Unsubscribe
Publish

## Slide 21: Connect
Client ID
Clean Session?
Username and Password
Keepalive Duration
Last Will and Testament

## Slide 22: Keep Alive
TCP/IP does not always notify when a socket breaks.
Broker could think connection is alive but really is dead.
Client must send a command or keepalive message periodically (defined by client at connection)
Max keepalive is 18h 12m 15s (65535 seconds)

## Slide 23: Client Takeover
When a client connects using the same client id of a session that the broker thinks is still connected.
Previous session is closed
New connection takes over previous session

## Slide 24: Last Will and Testament
MQTT often used in environments with loss of connectivity
  Unreliable networks
  Battery dies
  Equipment failure
What if your publisher suddenly goes offline?

## Slide 25: Last Will and Testament
Message to broadcast if a client goes offline:
  If server detects I/O or network failure
  Client fails to communicate within Keep Alive timeout
  Client closes without an appropriate DISCONNECT first
  Server closes the connection because of a protocol error
The Broker will publish one last message on your behalf

## Slide 26: PUBLISH
Topic name
QoS
Retain Flag
Payload (Binary)

## Slide 27: Topics
pipeline/3/pump/1239/temperature
Hierarchy string with / delimiters (resembles a directory path)
No “root” slash needed – just wasting space
Case sensitive!

## Slide 28: Quality of Service (QoS)
0: At most once delivery
1: At least once delivery
2: Only once delivery

## Slide 29: Quality of Service (QoS)
http://www.hivemq.com/blog/mqtt-essentials-part-6-mqtt-quality-of-service-levels

## Slide 30: Quality of Service (QoS)
http://www.hivemq.com/blog/mqtt-essentials-part-6-mqtt-quality-of-service-levels

## Slide 31: Quality of Service (QoS)
http://www.hivemq.com/blog/mqtt-essentials-part-6-mqtt-quality-of-service-levels

## Slide 32: SUBSCRIBE
QoS
Topic(s) to subscribe to

## Slide 33: Wildcard Characters
Wildcards for subscriptions: # and +
Example: pipeline/3/pump/+/temperature pipeline/3/pump/1239/temperature pipeline/3/pump/4445/temperature pipeline/3/pump/3224/temperature
Example: pipeline/3/# pipeline/3/pump/1239/temperature pipeline/3/pump/1239/pressure pipeline/3/valve/1239/state

## Slide 34: Persistent Connection
When Clean Session Flag = False during CONNECT:
  All subscriptions are maintained while offline
  All QoS 1 & 2 messages not confirmed by client will finish up upon reconnect
  All new QoS 1 & 2 sent while offline will be saved and sent upon reconnect
Note: QoS 0 subscription messages are not preserved while offline

## Slide 35: Publisher/Subscriber Decoupling
IoT Device
Application
Mobile Device
Web App
Broker
Publish QoS 1
Publish QoS 0
Publish
Publish QoS 2
Subscribers
Publisher
Sensors
Publisher
"Subscriber"
"Publisher"
Subscriber

## Slide 36: Facebook Messenger Story

## Slide 37: Facebook Messenger
First implementation had issues with long latency. Was reliable but slow.
With only weeks before launch, refactored to use MQTT
Designed to use bandwidth and battery sparingly (important for mobile apps)

## Slide 38
“By maintaining a MQTT connection and routing messages through our chat pipeline, we were able to often achieve phone-to-phone delivery in the hundreds of milliseconds rather than multiple seconds”
– Lucy Zhang, Facebook
https://www.facebook.com/notes/facebook-engineering/building-facebook-messenger/10150259350998920/

## Slide 39: Web Apps

## Slide 40: Websockets
Communication protocol that provides full-duplex communication channels over a single TCP connection
Note: Not supported by all MQTT Brokers

## Slide 41: Eclipse Paho JavaScript Client
https://github.com/eclipse/paho.mqtt.javascript

## Slide 42: MQTT.js
https://github.com/mqttjs/MQTT.js

## Slide 43: Putting it all Together

## Slide 44: SparkFun BME280

## Slide 45
Publish
Sleep
Read Sensor
Web Page
Web Page
Web Page
Broker
readings/403539 { "t": 2471, "h": 45681,
"p": 998365
}
readings/403539 { … }
403539

## Slide 46: DEMO: MQTT Pub/Sub

## Slide 47: Contact Information
Jason Follas
Quicken Loans
jasonfollas@quickenloans.com
Twitter: @jfollas
This presentation and code can be found here: https://github.com/jfollas/mqttdemo
#10
#1

## Slide 48: Photo Credits
https://access.redhat.com/documentation/en-US/Fuse_Message_Broker/5.4/html/Getting_Started/files/FuseMBStartedKeyJMS.html
Shutterstock 172364009
https://www.ibm.com/developerworks/community/blogs/c565c720-fe84-4f63-873f-607d87787327/entry/tc_overview?lang=en
Pipeline and Hazardous Materials Safety Administration
http://www.unitedenergytrading.com/crude-oil-trading/pipelines/